## Slide 1: Rail Delay Problem Formulation
Jacob Heglund

## Slide 2: Problem Formulation

## Slide 3: Problem Formulation
We want to predict the delay of the entire rail network simultaneously
  More specifically, we will be predicting the delay of every train at it’s next stop
  At the same time, we will be considering the reactionary delay effects that trains have on each other
In order to consider the rail network simultaneously, we must first transform our available data into a usable form

## Slide 4: Data Transformation
The raw data is structured s.t. each train route is indexed by its stations
  This poses a problem because this local index does not transfer between two different train routes
  That is to say, train stations do not work as a global index
Our solution to this indexing problem involves switching to a global index
  We sample the raw data at set time intervals (for example, every T = 15 minutes) to form a time-indexed dataset

## Slide 5: Data Transformation
Example of station-indexed data for a single train
Example of time-indexed data for a single train

## Slide 6: Data Transformation
There are some problems that may arise from this time-indexed formulation
  How to predict multiple “stations” in the future?
    Solution: Choose N_future s.t. it captures the longest time gaps between stops
  Repeated predictions
    Our model will output the same “next station” prediction multiple times if a train does not each it’s next station within the time interval
Despite potential issues, time indexing is the best method for structuring the data for our particular problem formulation

## Slide 7: Data Transformation
A note on time indexing
  If a train is sitting at Station A, then Station A is considered as the “previous station”
    Why this definition?
    The arrival delay for Station A is in the past at that point in time, and we will be predicting the arrival delay at the next station
    Therefore this definition makes sense given a time-indexed dataset

## Slide 8: Problem Formulation
We formulate the problem as a regression problem
  We plan to use similar metrics from Simon’s first paper to allow a direct comparison of results
    RMSE, MAE, MAAPE (mean arctan percentage error)
We propose the following features
  Input: z-score of arrival delay (in minutes) at the previous N_past timesteps
  Output: predicted z-score of arrival delay at the next N_future stations
    N_past and N_future are the number of timesteps as input and output respectively

## Slide 9: Problem Formulation
This work will include multiple input and output features as well
  This allows a direct comparison with Simon’s paper
  Input: takes the form as seen on page 10 of the paper
  Output: contains the variables predicted in the paper
    Deviation from arrival, deviation from departure, travel time, dwell time

## Slide 10: Graph Formulation
There are complicated interactions in the rail network
  These interactions are difficult to model directly
  Therefore, we use a graph neural network to implicitly account for these interactions
  This is done by training on past rail network data
A graph G(V, E) is defined by it’s nodes (or vertices) and edges
We define the nodes as follows
  Each node is a unique train route scheduled during the data period
    A route is said to be unique if the starting station, ending station, and starting time are different from all other routes in the data period
    This formulation gives a constant number of N nodes on the graph for the data period

## Slide 11: Graph Formulation
The adjacency matrix defines the connections between nodes on the graph
  These connections are referred to as “edges”
We define the graph edges as follows
  A(i, j) = 1 if train i and j are “interacting”
  = 0 otherwise
  “Interacting”: two trains are said to be interacting iff:
    They are travelling in the same direction
    Both trains are scheduled to arrive at the same station within some time radius Δ of each other
      Might need to consider “two trains have either the same previous stop and / or the same next stop” if time radius is difficult to establish

## Slide 12: Graph Formulation
“Travelling in the same direction”
  Create enumeration f which maps each station with an index
    f(A) = 1, f(B) = 2, f(C) = 3, f(D) = 4
Example
  Train #1 with origin-destination (OD) pair (A, D) will have a starting-ending difference of 1-4 = -3
  Train #2 with OD pair (C, A) will have a starting-ending difference of 3-1 = 2
  We will refer to this value as OD_diff
  Therefore,
    Routes with positive OD_diff travel eastward
    Routes with negative OD_diff travel westward
A
B
C
D

## Slide 13: Graph Formulation
“Travelling in the same direction”
  Two routes are said to be travelling in the same direction if the OD_diff of both routes have the same sign
    This definition is possible because there is a strict order of stations in our dataset
    Stations included in this study are intersected by the red line below
http://www.projectmapping.co.uk/Reviews/Resources/GWR%20HEX%202019%20Map%20-%20Image%20(1.png

## Slide 14: Graph Formulation
“Both trains are scheduled to arrive at the same station within some time radius Δ of each other”
  This part of the definition was chosen to help model reactionary delay effects in the rail network
Reactionary delay is difficult to model
  It involves complex feedback between trains that is not well-understood
This condition captures important aspects of train interactions at stations
  This allows the neural network model to implicitly compensate for reactionary delay in its predictions

## Slide 15: Problem Specifics
We now define preliminary values for variables defined in the previous slides
  T = 5 (minutes between data samples for index transformation)
  N_past = 12 (number of model input timesteps)
    This means our model could start predicting N_past * T minutes after the data for each day begins
  N_future = 1 (number of model outputs)
    i.e. delay at the next station
  Δ = 30 (time radius for two interacting trains in minutes)

## Slide 16: Solution Approach

## Slide 17: Model Architecture
We use a graph neural network to predict the rail network delays simultaneously
Our problem falls under the taxonomy of a “Time-Varying Spatio-Temporal (TVST) Graph”
  OR DYNAMIC ST GRAPH
  Time-Varying: Graph edges may change over time, giving a time-varying adjacency matrix A = A(k)
  Spatio-Temporal: Node features (also called spatial data) may change over time, giving a time-varying feature matrix X = X(k)

## Slide 18: Proposed Model Architecture
There are multiple relevant timescales for the rail network prediction problem
  Hourly, daily, weekly data are all relevant
  Each sub-model would capture information at the appropriate timescale
  Information is then fused together in the output layer
Sub-Model Input
(Xh, Ah)
Sub-Model Input
(Xd, Ad)
Sub-Model Input
(Xw, Aw)
Sub-Model (hourly)
Sub-Model (daily)
Sub-Model (weekly)
Fully
Connected
Fully
Connected
Fully
Connected
Feature Vector
Concat
Output Layer
Model Prediction

## Slide 19
Sub-Model Input
(Xh, Ah)
Sub-Model Input
(Xd, Ad)
Sub-Model Input
(Xw, Aw)
Sub-Model (hourly)
Sub-Model (daily)
Sub-Model (weekly)
Fully
Connected
Fully
Connected
Fully
Connected
Feature Vector
Concat
Output Layer
Model Prediction

## Slide 20: Proposed Model Architecture
Our architecture takes a stacked-block form
  Deeper architectures have not shown the same effectiveness for graph networks as with CNNs
  To reduce training overhead, an architecture with 2 TVST blocks would be reasonable
    If our architecture were deeper, we would employ skip or dense connections between blocks to improve training
Sub-Model Input
(X, A)
Sub-Model
Sub-Model Output
TVST Block
TVST Block
…
TVST Block
TVST Block

## Slide 21: Proposed Model Architecture
Temporal
Spatial
Temporal
Block Input
X, A
Block Output
ŷ[k]
The basic building block of the architecture is shown below
  Temporal = gated dilated causal temporal conv or temporal attention
  Spatial = Spatial Attention (“spatial” graph convolution)
  These methods are discussed in more detail in the following slides
residual connection

## Slide 22: Proposed Model Architecture
Spatial Aggregation Method
  Multi-headed attention
    Learns an importance weighting between a node and its neighbors
    Creates an embedding of the information contained in the nodes
    Allows the prediction of a graph as the output of the network
  Why this method?
    Effectively transmits information along the edges of a graph
    Able to adapt to the changing graph structure

## Slide 23: Proposed Model Architecture
Temporal Aggregation Methods
  Dilated, causal, gated temporal convolution
    First proposed in WaveNet (van den Oord, 2016)
    Computationally inexpensive to train compared to RNN while effectively capturing temporal information
    Used in state-of-the-art ground traffic forecasting papers
  Temporal Attention
    Learns an importance weighting on input-timesteps and predictions
    Used in state-of-the-art ground traffic forecasting papers